## Slide 1
OFF-GRID VEHICLE TRACKER
Weeks 1–2 Engineering Report
Capstone Project Lab · Group 9 · Sponsor: Dr. Richard Gale
Deo
Protocol Firmware
Josiah
Display & Navigation
Victor
Radio & Hardware
Cannon
Integration & Test
Fully off-grid direction-and-distance tracking between two vehicles — no cell, no WiFi, no infrastructure.

## Slide 2
Project Objective & Evaluation
Design, build, and field-validate a fully off-grid system that continuously shows a driver the direction and distance to a partner vehicle, across multi-km terrain with no communications infrastructure.
Engineering requirements
R1
No infrastructure: license-free 915 MHz ISM link, vehicle-to-vehicle
R2
Driver-glanceable: arrow + distance + data age, sunlight-readable
R3
Wireless in-cab link between radio unit and display unit
R4
Multi-km range in terrain (2–8 km design target, LOS ≫)
R5
Vehicle-powered; graceful degradation on any failure
How the project is evaluated
Weekly
15 progress presentations (W1–W15) — engineering content, hours & budget tracking
~W8
Midterm review: bench-integrated system demonstration
W8–W12
Field evidence: two-vehicle drive tests + range characterization data
Dec 10
Demo Day (W16): live end-to-end demonstration for the sponsor
W15–16
Final report: design, analysis, measurements vs. predictions
Success criteria (measurable)
Live position exchange at ≥ 2 km in terrain (PDR ≥ 90%)
Vehicle-relative arrow correct vs. GPS ground truth
Data age ≤ 60 s in normal operation, always displayed

## Slide 3
System Architecture
VEHICLE A
Heltec V4 — radio node
ESP32-S3 · SX1262 LoRa · GNSS
stock Meshtastic firmware
BLE (in-cab)
Waveshare 4.2″ RLCD — display
our only custom firmware
VEHICLE B
Heltec V4 — radio node
ESP32-S3 · SX1262 LoRa · GNSS
stock Meshtastic firmware
BLE (in-cab)
Waveshare 4.2″ RLCD — display
our only custom firmware
LoRa 915 MHz · AES · mesh
Why this architecture
Meshtastic Client API: documented protobuf stream over BLE — the same interface its phone apps use. No firmware fork.
One custom-firmware surface (the display). GPS, encryption, radio timing, mesh relay all ship pre-tested.
Any third node (ridge relay, hiker) extends range automatically — mesh for free.
Reflective LCD: sunlight-readable on a dash where TFTs wash out; fast enough for a live arrow.
Protocol stack
APP
Position payload (protobuf, ~40 B)
NET
Managed flooding · hop limit 3 · AES-256
MAC
CSMA, SNR-weighted backoff
PHY
LoRa chirp spread spectrum · 915 MHz ISM

## Slide 4
Team Roles & Semester Timeline
Deo
Protocol firmware: Meshtastic BLE client, protobuf decode, TrackerState feed
Josiah
Display & navigation: RLCD rendering, arrow UI, distance/bearing/heading math
Victor
Radio & hardware: Meshtastic config, GNSS, presets, antennas, range campaign
Cannon
Integration & test: bench rig, logging harness, drive tests, reports
W1
W4
W8
W12
W16
Deo
protocol core
hardening
Victor
bring-up + antennas
range tests
final char.
Josiah
display + nav + arrow UI
polish
Cannon
bench
integration + drives
install
report
risk gate
bench demo
Demo Day
Parallelism by design: the TrackerState contract decouples all four lanes from week 2 — no lane waits on another until bench integration (W7).

## Slide 5
Weeks 1–2 · Shared Foundations
The interface contract (agreed W1–W2)
struct TrackerState {
Fix self; // own GPS: lat lon course speed
Fix partner; // via LoRa: lat lon age_s
bool ble_connected;
};
One writer (protocol task) · one reader (UI task) · changed only by joint commit. This is what lets all four lanes build in parallel.
Process: every interface testable in isolation
Interface | Independent test (no custom code)
GPS → radio | Fix visible on radio OLED + phone app
LoRa A ↔ B | Two phone apps see each other's position
BLE Client API | Meshtastic Python CLI from a laptop
State → UI | Simulated TrackerState scenarios
Foundations in place
Shared git repo + CI-ready layout
PlatformIO toolchain (ESP32-S3)
nanopb + Meshtastic protobuf schema
Equipment received & bench-verified

## Slide 6
Weeks 1–2 · Individual Lanes
Victor — Radio & Hardware
7 h logged
Radio #1 flashed with Meshtastic (US-915) and configured
GNSS module integrated — 7-satellite fix verified, position on map via client app
Radio #2 flash & mesh position exchange next
Josiah — Display & Navigation
7 h logged
4.2″ reflective LCD panel driven from vendor BSP (ST7305, SPI, 400×300)
1-bpp framebuffer in PSRAM; full-screen refresh path working
Rendering layer + nav math implementation queued for W3
Deo — Protocol Firmware
7 h logged
nanopb toolchain built; Meshtastic protobuf schema compiled into project
Client API mapped: GATT service + ToRadio/FromRadio/FromNum characteristics
BLE central bring-up begins W2–W3 per plan
Cannon — Integration & Test
7 h logged
Bench rig assembled; both boards on instrumented USB power
Found & documented low-load shutoff hazard in USB chargers (affects 12 V adapters)
Range-test data collection plan drafted with Victor

## Slide 7
RF Link Engineering — Can We Reach 8 km?
Link margin closes when path loss reaches:
Preset | SF / BW | Bit rate | Sensitivity
SHORT_FAST | SF7 / 250 kHz | ~11 kbps | −121 dBm
LONG_FAST (default) | SF11 / 250 kHz | ~1.07 kbps | −129 dBm
LONG_SLOW (reserve) | SF12 / 125 kHz | ~0.18 kbps | −137 dBm
Each SF step ≈ +2.5–3 dB margin at ~½ the data rate. The payload needs only ~13 bit/s — capacity is deliberately traded for link margin (chirp spreading gain decodes up to 15 dB below the noise floor).
Chart: Path loss vs distance (km) — 915 MHz
| 1 | 2 | 5 | 10 | 20 | 50
Free space (20 log d) | 91.7 | 97.7 | 105.7 | 111.7 | 117.7 | 125.6
Two-ray, h=2 m (40 log d) | 108 | 120 | 136 | 148 | 160 | 176
Link budget ceiling (161 dB) | 161 | 161 | 161 | 161 | 161 | 161
Prediction: LOS reaches tens of km; ground-level two-ray crosses the budget near ~20 km; terrain diffraction sets the honest 2–8 km target. Victor's W3–W5 campaign measures this curve.

## Slide 8
Navigation Engineering — From Two Fixes to One Arrow
Great-circle distance (haversine):
Initial bearing (true-north referenced):
Driver's vehicle-relative arrow:
Heading from GPS course-over-ground — a magnetometer inside a steel cab is unreliable; COG is accurate above ~5 mph, and a driving product is usually moving.
Stationary fallback: north-referenced compass display when v < 2.2 m/s.
No ACKs by design: a newer position supersedes an older one — the correct reliability metric is data age (staleness), always shown to the driver.
N
own course (COG)
bearing θ to partner
arrow ∠ = θ − COG
Vehicle-relative by subtraction — no compass hardware needed.

## Slide 9
Week 3 Plan & Risk Management
Deo
BLE central bring-up: scan, connect, bond with radio; begin FromRadio decode. THE critical-path milestone (W3–W5).
Victor
Radio preset trade study (LONG_FAST vs LONG_SLOW) + broadcast-interval selection (30–60 s airtime analysis).
Josiah
Implement + unit-test nav math (haversine, bearing, COG heading); rendering layer setup.
Cannon
Bench instrumentation continues; range-test logging harness design (RSSI/SNR/PDR capture).
RISK GATE — Week 5
BLE bonding with Meshtastic is the project's highest-uncertainty item.
Decision rule: if pairing is still blocked after 2 weeks, switch transport to Meshtastic's identical API over WiFi/TCP :4403.
Only the transport layer swaps — decoder, state, and UI are untouched.
28 h
team hours logged (7 × 4)
$37.4k
budget estimate (TDL+TDM+ETRM)
$9.5k
computing in direct materials
46
tracked tasks on live Gantt