## Slide 1
OFF-GRID VEHICLE TRACKER
LIVE DEMO · TWO-VEHICLE DRIVE TEST
Recorded 2026-10-04, Lubbock TX. Every screen in these videos is live hardware:
two Meshtastic radios on a private 912.875 MHz LoRa channel, two custom displays. No phone, no internet, no network.
GROUP 9 · CAPSTONE PROJECT LAB · SPONSOR: DR. RICHARD GALE
Notes: Everything you are about to see is live hardware recorded Saturday night. Two radios, two displays, zero infrastructure.

## Slide 2
Link Up: The Partner Pulls Away
One minute of live tracking, no network anywhere.
Radio SF and its display, side by side and live. Top right: SF<->RG OK means the radios are actively hearing each other.
RG drives away: 621 ft becomes 0.30 miles on screen, position updates every 10 seconds while moving.
"age 7s" is the honesty meter: how old the partner's last report is. Single digits means the link is fresh.
"apart 15 mph" is computed on the display from consecutive positions, nobody transmits a speed-apart number.
Notes: Point at the age number first. Everything on this screen arrives over our private LoRa channel and gets decoded on the display itself.

## Slide 3
The Status Page: Everything the Link Knows
Full telemetry: positions, ages, battery, separation.
LINK CONNECTED, and below it: radios RG<->SF COMMUNICATING. Two different links, both named.
Both vehicles' live coordinates to five decimal places, each with its own data age.
RG reports its battery over the air: 95 percent. A dying partner radio warns this screen first.
573 ft between vehicles, and in words: SF IS S OF RG. Readable at a glance, at night, on a reflective panel.
Notes: This is the engineer page. Judges can check the coordinates against a map if they want, these are real fixes.

## Slide 4
Driving With It: The Convoy Page at 17 mph
The display talks like a driver, not like a GPS receiver.
Shot while actually driving: "you 17 mph" is our own GPS speed.
"0.27 Mi at 3 o'clock": the partner's direction in windshield terms, not map terms.
Blinker chevrons and the CHANGE COURSE banner fire when we drive away from the partner for 5 seconds.
"holding" means the gap is steady: the display smooths closing speed so GPS jitter never flaps the label.
Notes: This clip is why the UI uses clock positions and banners: at 17 mph nobody reads coordinates.

## Slide 5
Separation, Honestly Reported
What losing ground looks like on the glass.
The partner drives off: "apart 13 mph", distance climbing through 0.26 miles.
The age keeps counting between packets, and past the threshold the arrow hollows: estimate, not measurement.
The screen never pretends. Stale data looks stale, by design.
Note: this footage predates our course-up compass update, we held the unit rotated to match the road. The firmware now rotates the compass instead of the driver rotating the display.
Notes: If asked about the flipped handling in raw footage: that drive test is exactly what triggered the course-up firmware fix, shipped the next day. Iteration from road testing.

## Slide 6
Closing the Loop
Coming back together, guided by the arrow.
The return leg: "closing 13 mph", 0.37 miles down to 546 ft.
Radio and display in one frame: the radio's OLED shows 1 online and channel utilization in single digits, airtime budget holding.
From parked link-up to separation to reunion: one continuous session, zero reconnects, zero touches.
Next milestone: the open-road range test, measuring signal-to-noise versus distance against our link budget prediction.
Notes: Close with the thesis: nothing between the vehicles but physics and agreement. Then invite questions on the range test plan.